Harebot Bringup Checklist
Note: All code is in italics and enclosed in quotation marks, do not type the quotation marks.
Dependencies: ROS packages key_teleop(get it from GitHub) and Gmapping(get it from apt: “sudo apt-get install ros-indigo-slam-gmapping”
1. Plug in the white Netgear router.
2. Put fresh black NiMh Battery into slot on top of robot.
3. Connect jumper that is tied on the thin white cable into the connector on the end of the cable.
4. Connect the battery connector from the battery to the connector on the top of the robot.
5. Connect the laptop to the network with the SSID “Robot”, the password is the standard password d******5.
6. On the laptop, open a terminal and type in “ssh odroid@192.168.1.99” The password is [redacted]. This is the robot terminal.
7. In the robot terminal, run the command “cat ~/.bashrc” and verify that the line that starts with “export ROS_HOSTNAME=” has 192.168.1.99 as the address. Also verify that the line that starts with “export ROS_MASTER_URI=” has 192.168.1.99 as the address.
8. Start the roscore by running the command “roscore &” The & symbol send the job to the background so the terminal can be used to start the robot.
9. Wait 10-15 seconds until lines stop printing out on the screen then press enter and enter the command “clear”
10. Press the circular ON button in the top middle of the iRobot Create.
11. Run the command “roslaunch harebot_bringup harebot.launch” This command launches the robot.
12. Open a new terminal in the laptop and run the command “rviz” This launches the ROS visualization software, allowing the viewing of the map and SLAM data.
13. In a new terminal run the command “rosrun key_teleop key_teleop.py key_vel:=/cmd_vel” This starts the teleoperation code and you can control the movement of the robot using the arrow keys from this terminal.
14. In a new terminal run the command “rosrun gmapping slam_gmapping” This starts the actual SLAM
15. In RVIZ, click add in the left lower panel. Then add a map element. Press OK to add it to the map.
  Harebot Shutdown Checklist
1) Close any running processes by pressing Ctrl+C in the terminals. It may take up to 20 seconds for a process to shutdown.

2) Shutdown the Odroid by executing “sudo shutdown -h now” in the terminal. The sudo password is [redacted].

3) Power off the robot by disconnecting the battery connector from the black NiMh battery, and by disconnecting the jumper from the end of the white cable.